## Slide 1
Re-evaluation of airborne GEOPHYSICAL SURVEYS IN THE Edwards and Trinity Aquifers:
A collaborative project with the EAA and USGS
Marcus Gary
David V. Smith
EAA Board of Directors – Technical Briefing
April 11, 2017

## Slide 2
Data Acquisition and initial data reporting
2002
2003
2005

## Slide 3: Survey area in Medina and Uvalde counties

## Slide 4: High Resolution Aeromag Survey
Passive sensing of magnetic anomalies on surface and in subsurface

## Slide 5: Mag survey subdivided into manageable blocks
The entire survey was subdivided into smaller blocks for inversion modeling.

## Slide 6: Test analysis in block 6
Very small anomalies were not covered by sufficient flightlines (shown in black) for inversion modeling.
Ten study areas were extracted for inversion modeling.

## Slide 7: Preliminary EarthVision Modeling
Single anomaly
Multiple anomalies
Single anomaly with
Body Parameters shown at top
Dimensions and locations of model bodies (vertical pipes in these cases) are automatically adjusted until the modeled anomaly (red line) closely matches the airborne data (black line).

## Slide 8: The inversion results for the 16 blocks, with depth to top of bodies depicted with dot symbols
Dot Symbols
Blue = shallow
Yellow = medium
Orange = deep

## Slide 9: Surface geologic map with depth symbols
Dot Symbols
Blue = shallow
Yellow = medium
Orange = deep

## Slide 10: Geologic map with depths to anomalies
Dot Symbols
Blue = shallow
Yellow = medium
Orange = deep
USGS Knippa Gap Report
SIR2013-5149

## Slide 11: Multiple Anomalies
These anomalies appear to be isolated bodies, but notice how a deeper body feeds the shallow anomaly in the southwest.

## Slide 12: Sabinal Anomaly
This cluster of anomalies appear to be connected to a deeper source.

## Slide 13: Deep Creek Anomalies
Although appearing isolated, these anomalies are connected to the same parent body.

## Slide 14: Castroville Anomalies
Notice how deeper bodies appear to feed the shallow meandering feature.

## Slide 15
Camp Bullis AEM Study

## Slide 16
LITH. UNIT | All karst features (#) | High (#) | Medium (#) | Low (#) | Area (km2) | Karst Feature Density (features/ km2)
Kkk | 10 | 0 | 5 | 5 | 0.159 | 62.78
Kkd | 279 | 33 | 88 | 158 | 8.688 | 32.11
Kkb | 68 | 6 | 24 | 38 | 3.523 | 19.30
Kgr(u)A | 75 | 1 | 15 | 59 | 12.354 | 6.07
Kgr(u)B | 78 | 4 | 9 | 65 | 34.662 | 2.25
Kgr(u)C | 16 | 2 | 3 | 11 | 5.580 | 2.87
Kgr(u)D | 268 | 51 | 104 | 113 | 33.311 | 8.05
Kgr(u)E | 2 | 0 | 0 | 2 | 1.328 | 1.51
Kgr(l) | 168 | 38 | 75 | 55 | 13.907 | 12.08
TOTAL | 964 | 135 | 323 | 506 | 113.511 | 16.33
Karst feature mapping at Camp Bullis identified >1,200 features.
Recharge sensitivity ranked low, medium, and high based on numerous geologic and hydrologic factors.
Karst feature density is calculated for each mapped geologic unit (Edwards outcrops highest).
KARST FEATURE MAPPING

## Slide 17: Camp Bullis Karst Database
Geologic Map
Karst feature
Cave

## Slide 18
Cibolo Creek DIRECT CURRENT RESISTIVITY Surveys
Cibolo Creek is ephemeral, and rapidly recharges the aquifers during storms and wet periods.
Surveys were conducted at injection points for tracer studies (Jabba’s)

## Slide 19
Help from UT Karst Class
Suevey of two major karst recharge features

## Slide 20
BULLIS HOLE CAVE MAP

## Slide 23
JABBA’S GIANT SINK CAVE MAP

## Slide 25
Camp Bullis AEM Study

## Slide 26
Airborne Electromagnetic Geophysics
4. Resistivity depth cross sections - Interpretation of collected data
1. Conceptual model- Flight and survey planning
2. Ground based characterization – refine survey plan
3. Completion of flight survey (data collection) – contractor deliverables
5. Three-dimensional representation for hydrogeologic framework

## Slide 27: Contemporary AEM systems
12 m
GeoTEM
SkyTEM
AeroTEM
HeliTEM
VTEM
RESOLVE

## Slide 28
AEM Systems: Relative Footprints and Depths
Small
Target
Hectares/hr:
810 720 3200 6500
RESOLVE
Frequency domain
SkyTEM
Time domain
TEMPEST
MEGATEM
Depth of investigation depends on earth conductivity and target size.
100m
Notes: The system “footprints” shown here are approximations of the volume of earth that an AEM system samples as it flies. The volume of ground sampled by a fixed-wing time domain system is much larger, and the depth of exploration much greater. However, if the target is small like the red dot, then the volume of the footprint filled by the target is proportionately much greater for the HEM system, so the response of the target relative to the background will be greater. The smaller footprint also provides for higher resolution.
HEM systems are best for near-surface, smaller objects and high resolution. The FW-TDEM systems are better for great depth of penetration.

## Slide 29: AEM Principles
Transmitter creates time-varying magnetic field (white lines).
The primary magnetic field permeates the earth.
The changing magnetic field induces eddy currents in electrically conductive earth and discrete bodies.
The eddy currents generate secondary magnetic fields (black lines).
The secondary magnetic fields are detected and recorded by a receiver coil.
Signal strength is a function of transmitter power, coil sizes, height of the system above ground, and the electrical conductivity structure of the earth.

## Slide 30
Depth Sensitivity of AEM Systems
Shallow
~1-5 m
Deep
~500 m
RESOLVE system

## Slide 31
(Raw data)
(Processed data)
Final product
2D & 3D
visualizations
(Resistivity
per X, Y, Z)
Notes: This shows the progression from flying the HEM data (a), to recording the frequency dependent responses of inphase and quadrature at each point approximately every 3 meters (b) to numerical 1-D inversions of conductivity with depth (c) to constructing a color coded 3-D block of conductivity with depth for the entire flight area (Adapted from Fitterman, D. V. and M. Deszcz-Pan (1999), Geophysical Mapping of Saltwater Intrusion in Everglades National Park: Proceedings of the 3rd International Symposium on Ecohydraulics CDROM.
31

## Slide 32: Interpreting Resistivity Values
Resistivity
Lithology
Porosity
Salinity
Permafrost
Saturation
Grain
sorting
?
?
?
?
?
?
high
low

## Slide 33: Status of Project
All 1145 karst features in EAA database have been annotated on individual resistivity-depth sections.
Analyze clusters of karst features with respect to mapped geology and faults.
Correlate karst occurrence with resistivity zones and variations.

## Slide 34: Camp Bullis Karst Feature Database
Gridded Map

## Slide 35: Karst Features within 50 m of Flightlines
Databases also compiled for 10 m and 20 m distances.
Mapped karst feature
No karst mapping done south of Camp Bullis
Close-up

## Slide 36: Apparent resistivity at 115 kHz
Mapped geologic features (contacts, faults) are shown as black lines
This, the highest of the 6 HEM frequencies, senses shallow variations in earth electrical resistivity.

## Slide 37: Resistivity-depth Inversions
Both classical smooth multi-layer inversion (using EM1DFM) and novel Markov-chain Monte-Carlo (MCMC) probabilistic methods were employed to compute resistivity-depth profiles
EM1DFM
MCMC
MCMC
EM1DFM
Line 10620
Line 10640
Line 10640 path over geology

## Slide 38: Inverted Resistivity at Depth Below Ground Surface
10 m BGS
40 m BGS

## Slide 39: Inverted Resistivity at Fixed Elevation Above Mean Sea Level
Resistivity slice at 340 m AMSL
Resistivity slice at 340 m AMSL

## Slide 40: Curtain Diagram of Inverted Profiles

## Slide 41: Working within Geosoft
Single resistivity-depth profile
This database is of karst features within 50 m of flightline. Note ‘ID’ and distance ‘Dist’ are tabulated.
Window for map viewing
Close-up of map window
Window for selecting maps
Database of resistivity-depth
profiles
20-m wide box at each feature,
labeled with ID and Distance

## Slide 42: Resistivity-Depth Sections (left justified)
Lines 10230 - 10400
Lines 10010 - 10220
Lines 30010 - 30190

## Slide 43
Lines 10410 - 10540
Lines 10550 - 10740
Lines 30360 - 30380
Lines 30200 - 30350
Resistivity-Depth Sections (left justified)

## Slide 44: Correlating Resistivity Zones with Karst Features
Numerous karst features mapped in blue (low resistivity) zone
Possible karst features present in blue (low resistivity) zone?

## Slide 45
EARLY ESTIMATES OF UPLAND RECHARGE VALUES
Based on a “typical” 2.7 cm rain event.

## Slide 46
Δh
ΔS
river
Qin
Qout
ΔS
Well 10
Water Tank
Bunny Hole
Collaborative efforts between BEG, EAA, and DOD
POINT:
In situ data (23 stations)
H1D Model
FIELD/PLOT:
Eddy Covariance (3)
Shallow Geophysics
Drip rates
Stream/GW
CAMP BULLIS:
ET MODIS (1km)
ET/LAI Landsat (30m)
AEM ANALYSIS WILL BE INTEGREATED INTO DIFFUSE RECHARGE STUDY

## Slide 47: HEM System at Seco
Seco Helicopter
Seco Creek, Texas, HEM Survey
RESOLVE system
6 EM frequencies
400 – 100,000 Hz
Internal Magnetometer
High Resolution GPS
Laser Altimeter

## Slide 49
aquifer-wide recharge characterization with a regional AEM survey?

## Slide 50
APPLICATIONS OF A REGIONAL AEM GEOPHYSICAL DATASET
Ability to directly characterize the spatial variability of porosity and permeability on the surface and sub-surface.
Complementary dataset to refined geologic mapping of the Edwards and Trinity (on-going project)
Use of data to greatly improve recharge models, thus improving GW models
Dataset could be used as factor in determining recharge potential for conservation easement prioritization.
A regional survey would be expensive, but may be the best way to obtain a single dataset to characterize recharge potential across the entire system.
Possible to partner with other agencies/entities to fund this large project (CoSA, TWDB, TNC, GCDs, others….).

## Slide 51: Australia
Water Quality
Regional Scale

## Slide 52
Regional/National Scales

## Slide 53
Thank you!